## Slide 1: Satellitendaten in der Klimatologie

## Slide 2: Essential Climate Variables

## Slide 3: ECVs and Satellites (1)
ECV | Climate system component | Name of satellite | Name of intrument | Orbit type | Measurement type

## Slide 4: Surface wind speed and direction
What does it represent? Wind speed and direction at 10 m above ground, calculated from observation of backscatter from ocean surface
Which climate component does it belong to? Atmosphere, but measurement is taken at the interface between ocean and atmosphere
How is it measured/observed (name of satellite/instrument)? Measured by scatterometers like ASCAT (MetOp-A), SeaWinds (QuickSCAT)
Anything interesting (problems, fancy measurement techniques, ...)? SeaWinds was designed to work for two years, but it was working for more than ten years! You can see ships/shiptracks as artifacts in scatterometer data

## Slide 5: ECVs and Satellites (2)
ECV | Climate system component | Name of satellite | Name of intrument | Orbit type | Measurement type
Surface wind speed and direction | Atmosphere | QuikSCAT, MetOp-A,… | SeaWinds, ASCAT,… | LEO | active

## Slide 6: What are satellites?
In celestial mechanics:
A body of mass moving around another body of mass on an orbit.
Earth observing satellites:
Orbit Earth
do not measure variables such as temperature or ocean wave height directly
measure radiances or radar echoes

## Slide 7: How do satellites observe Earth?
Radio occultation observations
sending signals from one satellite to another
bending angle of signals crossing the troposphere or stratosphere depends on temperature and humidity
Active instruments
Send out signals and measure backscatter
Radar or lidar
Information on surface, clouds and winds
Passive instruments
Measure radiation emitted naturally
Information on temperature, humidity, clouds, surface conditions
Information on winds by motion tracing of clouds and cloud features
https://www.eumetsat.int/satellites-instruments
https://www.nasa.gov/directorates/heo/scan/communications/outreach/funfacts/txt_passive_active.html

## Slide 8: What are orbits?
Orbit types:
Low Earth orbit (LEO)
Medium Earth orbit (MEO)
Geostationary orbit (GEO)
Curved trajectories of objects, e.g.
Of a planet around a star
A natural satellite (moon) around a planet
An artifical satellite around a planet, moon, asteroid or Lagrange point
By Sedrubal - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=114587517

## Slide 9: How do orbits work? (1)
Simple circular Orbit
Centripetal force == force of gravity
https://doi.org/10.1016/B978-0-12-382225-3.00362-5
Newton's Laws of Motion
  Every body will continue in its state of rest or of uniform motion in a straight line except insofar as it is compelled to change that state by an impressed force.
  The rate of change of momentum is proportional to the impressed force and takes place in the line in which the force acts.
  Action and reaction are equal and opposite.
Newton's Law of Universal Gravitation
The force of attraction between two point masses and separated by a distance r is given by where is the Newtonian (or universal) gravitation constant (6.67259 × 10−11 ).
For large masses or high precision general relativity has to be included.

## Slide 10: How do orbits work? (2)
Example 2:A satellite in geosynchronous orbit has the same angular velocity as the earth:𝜉 = 2𝜋𝑇 = 7.292115×10−5 𝑟𝑎𝑑𝑠The radius for this orbit is 42 164 km (35 786 km above the Earth's surface).
Example 2:
A satellite in geosynchronous orbit has the same angular velocity as the earth:
The radius for this orbit is 42 164 km (35 786 km above the Earth's surface).
https://doi.org/10.1016/B978-0-12-382225-3.00362-5
How long does the satellite need for one rotation around Earth?
Circumference:
Speed is path per time:
Simple circular Orbit
Centripetal force == force of gravity
Example 1:
Typical meteorological satellite orbits 833 km above the Earth's surface (radius of Earth is 6378.137 km). This gives an orbit radius of about 7211 km.
This yields a period of about 102 minutes.

## Slide 11: How do orbits work? (3)
Keplers laws
All planets travel in elliptical paths with the Sun at one focus.
The radius vector from the Sun to a planet sweeps out equal areas in equal times.
The ratio of the square of the period of revolution of a planet to the cube of its semimajor axis is the same for all planets revolving around the Sun.
Elliptical Orbit
Eccentricity
https://doi.org/10.1016/B978-0-12-382225-3.00362-5

## Slide 12: How do I get to another Orbit?
By Phoenix7777 - Own workData source: HORIZONS System, JPL, NASA, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=71079277
By Leafnode - Own work based on image by Hubert Bartkowiak, CC BY-SA 2.5, https://commons.wikimedia.org/w/index.php?curid=1885233
Hohmann transfer

## Slide 13: How do orbits work? (4)
By cmglee - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=16891766

## Slide 14: Real orbits
Real orbits |  |  |  |  |  |  |  |  |  |  |  | 
Satellite |  | Semimajor axis (km) | Inclination (deg) |  | Eccentricity | Right ascension of ascending node |  | Argument of perigee |  | Mean anomaly |  | Nodal period (min)
Name | ID |  |  |  |  | Value (deg) | Motion (deg day−1) | Value (deg) | Motion (deg day−1) | Value (deg) | Motion (deg day−1) | Empty Cell
INSAT 3B | 00016B | 42 165.44 | 0.08 | 4.846 × 10−4 |  | 288.81 | −0.0134 | 233.08 | 0.0268 | 266.58 | 360.98 | 1435.97
GOES 8 | 94022A | 42 164.66 | 0.16 | 3.691 × 10−4 |  | 104.85 | −0.0134 | 61.66 | 0.0268 | 104.11 | 360.99 | 1435.93
GOES 10 | 97019A | 42 166.53 | 0.25 | 3.304 × 10−4 |  | 276.33 | −0.0134 | 248.95 | 0.0268 | 44.58 | 360.97 | 1436.03
METEOSAT7 | 97049B | 42 164.70 | 0.54 | 4.900 × 10−5 |  | 296.54 | −0.0134 | 68.78 | 0.0268 | 339.61 | 360.99 | 1435.94
GMS 5 | 95011B | 42 166.75 | 0.58 | 1.647 × 10−4 |  | 65.29 | −0.0134 | 259.00 | 0.0268 | 161.45 | 360.97 | 1436.04
FENGYUN 2B | 00032A | 42 167.40 | 0.94 | 9.130 × 10−5 |  | 264.49 | −0.0134 | 164.52 | 0.0268 | 20.73 | 360.96 | 1436.07
ELEKTRO | 97069A | 42 171.69 | 3.25 | 5.438 × 10−4 |  | 81.41 | −0.0134 | 138.84 | 0.0267 | 202.39 | 360.90 | 1436.29
TRMM | 97074A | 6 729.00 | 34.98 | 1.923 × 10−4 |  | 6.60 | −6.7736 | 293.05 | 9.7410 | 159.10 | 5666.31 | 91.33
UARS | 91063B | 6 948.65 | 56.98 | 5.552 × 10−4 |  | 45.52 | −4.0224 | 102.59 | 1.7883 | 87.93 | 5395.39 | 96.05
ERBS | 84108B | 6 953.02 | 57.00 | 8.553 × 10−4 |  | 330.37 | −4.0122 | 94.57 | 1.7807 | 59.04 | 5390.29 | 96.14
MOLNIYA 3-4 | 98040A | 26 554.87 | 63.08 | 7.285 × 10−1 |  | 126.09 | −0.1391 | 279.98 | 0.0038 | 221.47 | 722.21 | 717.79
METEOR 3-6 | 94003A | 7 572.34 | 82.56 | 1.542 × 10−3 |  | 252.61 | −0.7073 | 350.18 | −2.5018 | 335.10 | 4740.49 | 109.41
TERRA | 99068A | 7 077.71 | 98.18 | 3.067 × 10−4 |  | 326.40 | 0.9847 | 104.03 | −3.1085 | 207.77 | 5245.62 | 98.88
QUICKSCAT | 99034A | 7 180.38 | 98.63 | 3.750 × 10−5 |  | 73.99 | 0.9868 | 0.98 | −2.9189 | 264.67 | 5133.63 | 101.04
NOAA 15 | 98030A | 7 189.40 | 98.63 | 1.168 × 10−3 |  | 277.24 | 0.9828 | 44.01 | −2.9058 | 223.53 | 5123.98 | 101.23
FENGYUN 1C | 99025A | 7 233.57 | 98.73 | 1.495 × 10−3 |  | 289.04 | 0.9733 | 30.07 | −2.8357 | 135.06 | 5077.16 | 102.16
Epoch time = 0000 UTC 6 September 2000.
https://doi.org/10.1016/B978-0-12-382225-3.00362-5

## Slide 15: GEO orbits
GOES USA
Meteosat ESA, EUMETSAT
COMS-1 and GK-2A Republic of Korea
Elektro-L Russia
Himawari Japan
Fengyun China
INSAT India
…
https://www.dwd.de/DE/forschung/atmosphaerenbeob/wettersatelliten/satelliten_meteosat_node.html

## Slide 16: Video MTG UVN Animation

## Slide 17: MEO orbits: semi synchronous orbit
altitude of around 20,000 km
Period of about 12 hours
Used for GNSS because it is reliable predictable
GNSS (Global Navigation Satellite Systems):
Global Positioning System GPS (USA) at 20,200 km
Galileo (EU) at 23,222 km
BeiDou (China) at 21,528 km
GLONASS (Russia) at 19,100 km
https://www.dlr.de/rd/DesktopDefault.aspx/tabid-2439/3577_read-5294/gallery-1/gallery_read-Image.28.12160/

## Slide 18: Video "Galileo" en route to full operational capability

## Slide 19: MEO orbits: Molinya Orbit
GEO orbits not well suited for high latitudes
High eccentricity -> longer time period above high latitudes
Von Hartze11 - http://en.wikipedia.org/wiki/Image:Molniya.jpg, Gemeinfrei, https://commons.wikimedia.org/w/index.php?curid=1567383
By Phoenix7777 - Own workData source: Satellite Catalog (SATCAT), CelesTrak, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=89120635

## Slide 20: LEO orbits
Closer to the surface than GEO
Less energy needed to reach orbit
Small field of fiew
Orbital decay due to drag by atmosphere
Equatorial low Earth orbits (ELEO)
Low inclination to Equator
Rapid revisit times at low latitudes
Very few energy needed if prograde orbit
Polar orbits / Sun-synchronous orbits
High inclination
Cover (almost) all latitudes
Need more energy than ELEO orbits
https://www.remss.com/missions/ascat/

## Slide 21: Video NASA Earth Observing Fleet

## Slide 22: How do orbits work? (5)
https://imgur.com/gallery/pOGJGQv
By cmglee - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=16891766

## Slide 23: Homework
• More on satellite instruments:
https://www.eumetsat.int/satellites-instruments
• More information on Orbits:
• A short introduction to orbits can be found on https://www.esa.int/Enabling_Support/Space_Transportation/Types_of_orbits
• I used this paper to descripe how orbits work (there is an error in eq.
2):https://www.sciencedirect.com/science/article/pii/B9780123822253003625
• More information on how satellites actually look give the EUMETSATS "Meet the satellite" videos like this one on Sentinel-3
https://youtu.be/ZRxB5mSassg?list=PLOQg9n6Apif1HPiQfv3u_9ZJm5o4MxhY3
• Until next week please watch the following videos on
• Copernicus Climate Change Service
https://www.youtube.com/watch?v=5H_OncVxeSM
https://www.youtube.com/watch?v=dSnVJr6ZQ6M&list=PLB7XYEK5KkhrlxddeUOht-LmgnZ-PMB31&index=16
https://www.youtube.com/watch?v=CacbAL_lahs
• data access and processing
https://www.youtube.com/watch?v=E3XBb1D6dUM&list=PLOQg9n6Apif1HPiQfv3u_9ZJm5o4MxhY3&index=61
5
• the data format NetCDF and processing (part about Panoply)
https://www.youtube.com/watch?v=XqoetylQAIY
• Most datasets we will work on will be in NetCDF format. Please try to install Panoply to few this data https://www.giss.nasa.gov/tools/panoply/
• Familiarise yourself with the website of copernicus https://www.copernicus.eu/en/copernicus-services and have a look at thedifferent services they
offer.

## Slide 24: Nex week: Where can we find data sets?
https://www.copernicus.eu/en/copernicus-services